## Slide 1: AUTOMATED TEA BREWING SYSTEM

## Slide 3: PRESENTED BY:
ALEEHA AIMAN (23-NTU-CS-1243)
NAIMA NAVEED (23-NTU-CS-1032)
ESSHA IMRAN (23-NTU-CS-1022)

## Slide 4: Project Overview 1. IoT-based automated tea brewing system 2. Controls complete tea preparation process 3. Reduces manual effort 4. Provides smart and efficient solution 5. Operated through a web-based interface

## Slide 5: Objectives
Automate tea preparation
Improve efficiency and consistency
Provide easy user interaction
Enable remote control using IoT
Ensure safe system operation

## Slide 6: Technology Stack
ESP32 microcontroller
WiFi-based communication
HTML, CSS, JavaScript (Frontend)
ESP32 Web Server (Backend)
MongoDB (Cloud Database)
Relays, Servo Motors, SSR

## Slide 7: Key Features
Web-based control interface
Fully automated brewing sequence
Real-time status monitoring
Remaining time display
Pre-configured tea recipes
Emergency stop functionality

## Slide 8: Cloud Integration
Stores tea recipes
Saves user-selected favorite recipes
Enables quick recipe access
Provides centralized recipe management
Supports future cloud expansion

## Slide 10: Recipe & Customization options
Automatic Mode
Cloud-stored recipes
Cup selection
Manual Mode
Sugar selection
Milk selection
Water control
Adjustable tea strength

## Slide 11: System Architecture
Hardware Layer
  Pumps, servos, stove
Control Layer
  ESP32, relays, SSR
Software Layer
  Web interface
Cloud Layer
  MongoDB (Recipes storage)

## Slide 13: Hardware Components
ESP32 development board
2-channel relay module
DC water and milk pumps
Servo motors for ingredients
Stove for boiling
Solid State Relay (SSR)
Food containers

## Slide 14: Hardware Architecture
GPIO 27 → Water pump
GPIO 26 → Milk pump
GPIO 18 → Tea dispenser
GPIO 19 → Sugar dispenser
GPIO 23 → Stove control

## Slide 15: Software Architecture
Arduino framework (PlatformIO)
ESP32 WiFi library
WebServer library
REST-based communication
Web-based user interface
MongoDB for recipe storage
Mqtt and node-red

## Slide 16: MQTT & NODE-RED
MQTT was used for efficient real-time communication.
Node-RED handled message flow and system control in a visual and scalable manner

## Slide 22: Automatic Stove Control
Stove turns ON automatically
Ingredients collected in pan
Stove turns OFF after tea is ready
Controlled using SSR
Enhances safety and efficiency

## Slide 23: User Workflow
Power ON the system
ESP32 connects to WiFi
Open device IP in browser
Select recipe or manual mode
Click Start Brewing
Monitor brewing status
Collect tea after completion

## Slide 30
NETWORK
CONFIGURATION

## Slide 31: Challenges Faced
Motors not running
Servo motors not rotating
Incorrect timing issues

## Slide 32: Solutions Implemented
Relay and power verification
GPIO pin checking
Servo wiring correction
Mechanical inspection
Timing logic adjustment

## Slide 34: Conclusion
Successfully implemented IoT-based tea automation
Simple and user-friendly system
Reliable hardware and software integration
Cloud used effectively for recipe storage
System ready for future enhancements